## Slide 1: Polarimetry Influenced by CCN aNd INP in Cyprus and Chile (PICNICC)
An assessment of hemispheric contrasts in polarimetric Doppler cloud radar observations and its relation to differences in aerosol load
Bonn, October 23, 2019
PIs: Heike Kalesse, Patric Seifert, Johannes Quaas
PhD students: Teresa Vogl (Uni Leipzig), Audrey Teisseire (TROPOS)
Collaborators: Rodanthi Mamouri (Cyprus University of Technology, Limassol, Cyprus), Boris Barja (University of Magallanes, Punta Arenas, Chile)
Many other PhDs and researchers from
TROPOS and LIM are involved
Notes: Our SPP-PROM project, PICNICC project,
As the title suggests, aerosol influence on microphysics using polarimetric observables

## Slide 2: Outline
Motivation + Hypothesis + field campaigns
Work Plan + Status Report PhD1 – Teresa Vogl
Work Plan + Status Report PhD2 – Audrey Teisseire
Notes: Work planned for one of the two  Patric will continue

## Slide 3
aerosol particles
cloud droplets
ice particles
large ice particles
rain
The role of aerosol in mixed-phase cloud processes
Heterogeneous
ice nucleation
Riming
Aggregation
Multiplication
How do aerosols influence occurrence frequency of microphysical growth processes?
CCN... Cloud condensation nuclei
INP... ice nucleating particles
Notes: Availability of CCN and INP determines number conc. of cloud droplets and ice crystals
In the MPC T-range of Zero to -37C, ice formation happens via het. Ice formation processes for which CCN and INP are required (to form cloud droplets and ice particles).
The ice particles grow and form precipitation through w.v. deposition or aggregation or riming
Ice multipl. can also happen, e.g. through rime splintering.
Ice formation thus affects precip. formation and cloud rad. Prop. Depend on the amount + distribution of liquid+ice in the cloud.

## Slide 4
< 50 cm-3
~1000 cm-3
~100 cm-3
~1000 cm-3
present day
[Hamilton 2014 PNAS]
But how can we pin down potential aerosol effects?
 Study clouds under contrasting aerosol conditions
< 5 m-3
~ 100 m-3
[Vergara-Temprado 2017 ACP]
Mean concentration of INP at ground for -15°C (dust and marine biogenic)
Punta Arenas, Chile
Limassol, Cyprus
Punta Arenas, Chile
Limassol, Cyprus
Notes: - CCN availability over the Southern Oceans in the summer (Jan) is low, on the order of 100 cm-3, in the winter (Jul) even lower (<50 cm-3)
- This is in strong contrast to e.g. Central Europe or the Eastern Mediterranean (red star) where 1000 cm-3 are typical.
Hamilton 2014, PNAS:
- GCM study
PD = present day
Uncertainties: -Over marine regions, modeled uncertainty in CCN concentrations is typically 20–40% between ±60° latitude,
up to about 70–90% at higher latitudes and over 100% near Antarctica and high latitude Arctic regions. In some continental regions, uncertainties exceed 100% of the mean
in regions dominated by fires.
- we identify the southern Pacific Ocean (approximately 20°S–60°S, 90°W –180°W) as a large region close to pristine, especially during SH summer
when monthly mean PD CCN concentrations in this region are in the range of 53–285 cm−3
- In NH midlatitude regions, there are no pristine days at any time of the year
Yum and Hudson, 2014, JGR:
Tasmania, winter-summer contrasts of CCN based on aircraft obs.
Winter: mean CCN 30 cm-3;
(dry diameter above 50 nm and calculated at cloud base (∼915 hPa)  of what? Which paper?)
Vergara-Temprado, 2017 ACP:
- Global model of INP based on lab + field meas. of K-feldspar (active component) and marine organics
Annual mean distributions of ice-nucleating particles concentrations, for an activation temperature of -15 C based on
feldspar (a) and marine organics (b). Panel (c) shows the total INP concentration obtained by summing the INP concentrations from Kfeldspar
and marine organics. We show [INP]T for a T of -15 C because this is a temperature used by many instruments. The number
of INP that activate to ice crystals ([INP]ambient) at the surface will be zero over much of the globe, because these particles will
only become important at high altitudes. Surface concentrations are shown because this is where most observations of atmospheric INP
concentrations are made.

## Slide 5
middle east dust
40°S
DACAPO-PESO
Punta Arenas, Chile
MODIS at Aqua
22.01.2018
polluted continental
polluted marine
Saharan dust
CyCARE*
Limassol, Cyprus
Oct 2016 – Apr 2018
35°N 33°E
60°S
prevailing
westerly winds
Southern Ocean
53°S 71°W
8000 km
7° lat.
* Cyprus Cloud Aerosol and pRecipitation Experiment
Blue: Punta Arenas
Orange: Cyprus
Notes: …aerosol loadings are so different, that there is hardly any overlap in the AOT histograms. Thus those two locations are ideal to study impact of aerosols on e.g. ice formation processes in MPC

## Slide 6
35GHz cloud radar
Optical disdrometer
14 channel microwave radiometer
Ceilometer
94 GHz cloud radar
(LIM)
24 GHz micro rain radar
PollyXT lidar
Doppler
lidar
Savernet lidar
(UMAG)
radiation
station
+ sun photometer
upwind in-situ
sampling by TROPOS cloud group
LACROS: Leipzig Aerosol and Cloud Remote Observation System
LACROS at Punta Arenas, Chile
Measurement period:
Nov 2018 – likely March 2020
Not available at CyCare in Limassol, Cyprus
Notes: Let me now give you a brief overview of the instrumentation used:
Two instrument containiers…name instruments, MIRA: vpt + scanning; (Polly XT = multi-wl, depol lidar)
Additional instrumentation: … + 94 Ghz cloud radar  dual -freq. Doppler Radar obs. For studying microphy. Growth processes (more details later)
Bei den Aerosolinstrumenten: - es reicht zu wissen, dass es SMPS, CCNC und INP-Offline Filter sampler gibt. - Time Resolution 2-3days - die Filter werden von Raul bzw. Boris getauscht
SMPS: Scanning Mobility Particle Size Spectrometer: aerosol PNSD (RH < 40%), size range???
CCNC: CCN-counter

## Slide 7: Hypothesis: microphysical growth processes in Mixed-phase Clouds are susceptible to aerosol perturbations
High aerosol loads and high INP concentrations  higher ice crystal concentrations  more aggregation
2. Low aerosol loads and scarcity of INP  thicker/ more persistent supercooled liquid layers  more riming
www.inscc.utah.edu/~tgarrett/Snowflakes/Gallery/
aggregate
rimed ice particle
Notes: Precisely, two assumptions:
One the one hand, …
 Test these hypotheses using data from two field campaigns

## Slide 8
Investigating hemispheric differences in aerosol signatures in mixed-phase cloud processes with spectral polarimetric cloud radar observations
PhD student (1) : Teresa Vogl
Supervisors : Heike Kalesse, Patric Seifert

## Slide 9: TERESA Vogl, PhD 1

## Slide 10: Work package 1 (PhD 1): ANALYSIS OF BULK MOMENTS FOR MICROPHYSICAL FINGERPRINTING
Analysis of radar moments: Ze, VD,σ, LDR, skewness
Gradients of moments
Determination of VD-Ze power relations and comparison to existing relations for aggregation and riming (Straka et al., 2000)
Multi-frequency analysis (Dual-wavelength-ratio Ka/W)
Graupel
Aggregates
Doppler velocity (m/s)
Reflectivity (dBZ)
Oue et al., 2018
Straka et al., 2000
Notes: Bulk moments
Gradients along slanted fall streaks
Distinguishing riming and aggregation processes
Problem: strong vertical winds in P.A.

## Slide 11: Work package 2 (PhD 1): DOPPLER SPECTRA ANALYSIS
Active development of peak detection and tracking tools:
  PEAKO peak detection algorithm (Kalesse, Vogl et al., AMT 2019)
  peakTree tool for tracking peak properties (Radenz et al., AMT 2019)
PEAKO is a supervised machine learning framework for peak detection
peakTree also detects peaks and puts them into a binary tree structure
Using PEAKO peaks in the peakTree structure
Notes: WP2
Supervised means trained with input data from a user
Binary tree structure makes it easy to classify peaks; also moments are calculated for each peak

## Slide 12: Work package 2 (PhD 1): DOPPLER SPECTRA ANALYSIS
It is possible to select peaks fulfilling certain criteria.
35 GHz radar reflectivity, Punta Arenas, 2019-02-23
„liquid“ : peaks with
Z < 20 dBZ and
|v| < 0.3 m/s
Notes: Case from 2019-02-23 in Punta Arenas
Multi-peak situation

## Slide 13: Work package 2 (PhD 1): DOPPLER SPECTRA ANALYSIS
E.g. selecting possible liquid peaks
Reflectivity of „liquid“ population, Punta Arenas, 2019-02-23
Notes: e.g. we can extract peaks that are possibly liqud
Some have high ldr  fresh ice

## Slide 14: Work package 2 (PhD 1): DOPPLER SPECTRA ANALYSIS
It is possible to select peaks fulfilling certain criteria.
35 GHz radar reflectivity, Punta Arenas, 2019-02-23
„rimed“ : peaks more than 1.5 m/s faster than slowest falling peak
„tails“
Notes: Case from 2019-02-23 in Punta Arenas
Multi-peak situation

## Slide 15: Work package 2 (PhD 1): DOPPLER SPECTRA ANALYSIS
e.g. probably rimed population
Reflectivity of „rimed“ population, Punta Arenas, 2019-02-23
Notes: „riming“ node: e.g. in this spectrum the fastest and slowest peaks are more than 1.5 m/s fall velocity apart

## Slide 16: Work package 3 (PhD 1): Modeling
Cloud-resolving modelling with ICON-NWP
  case studies
  sensitivity study (variation of empirical parameters)
  simulation of full observation periods
  take NH aerosol conc. to SH and vice versa
Attribution of observations in NH and SH to differences in INP/ CCN
Limassol
Punta
Arenas
Notes: WP 3 : modeling
Are observed differences due to INP/CCN differences?
ECMWF: initial + boundary condition, CCN and INP from existing sources or TROPOS retrieval
First case studies, then sensitivity study

## Slide 17: Work package 3 (PhD 1): Modeling
Modeled 35 GHz reflectivity
spin up
Measured 35 GHz reflectivity
+ 7 dB
10 km grid resolution
Notes: Coarse domain (test domain) with 20 km horizontal resolution  we will eventually go down to 1.2 km
MIRA and PAMTRA reflectivity (of course LIMRAD failed exactly on the day for which I have IFS data)

## Slide 18: Challenges
Gravity waves: Punta Arenas site experiences very large vertical wind velocities
Attenuation by rain has to be corrected for to make dual-wavelength comparison possible (hardly any snow cases in data set)
„Tails“ in MIRA spectra
Absolute radar calibration…
Reflectivity
Mean Doppler Velocity
19:40 UTC
Picture: Heike Kalesse
Notes: Large vDop differences make e.g. liquid detection difficult
Tails cause all sorts of crap
For DWR studies, rain attenuation correction and radar offset calibrations are needed

## Slide 19
Investigation of the susceptibility of mixed-phase cloud processes to aerosol perturbations with scanning SLDR-mode cloud radar
PhD student (2) : Audrey Teisseire
Supervisors : Patric Seifert, Heike Kalesse
Notes: I am Audrey Teisseire, and I am the PhD 2 in the PICNICC project
My Phd is investigation …

## Slide 20: Audrey Teisseire, Phd 2

## Slide 21: Instruments
MIRA : 35 GHz scanning cloud radar in SLDR-mode
Scanning SLDR cloud radar Mira-35
Measures reflectivity, Doppler spectrum, slanted linear depolarization ratio (SLDR), Cross-channel correlation
Determines cloud structure, polarimetric hydrometeor typing, microphysical fingerprinting
Mira 35 GHz scanning radar - TROPOS
Notes: For my study I use a 35 GHz scanning cloud radar from 30 to 90 degrees (elevation angle) in SLDR mode.
Scanning radar is able to give me two essentials polarimetric parameters which are slanted linear depolarization ratio (SLDR) and Cross-channel correlation.
With these parameters I will use to determine the orientation and shape of observed particles.

## Slide 22
Ice physical properties
Shape and orientation estimation of ice crystal.
Unique relationship between: SLDR, rcx, antenna elevation angle and particle shape
Particle shape assumed to be spheroidal
(Myagkov et al, 2016a, AMT)
Notes:  The determination of SLDR and Rhocx gradient with elevation angle can inform us about the shape of particle (prolate or oblate) and orientation
 These two Ice physical parameters can be useful to determine the type of particle.

## Slide 23: Output with Alexander Myagkov‘ Algorithm
SLDR (Slanted Linear-Depolarization Ratio), dependency with orientation and shape of ice crystal
(Myagkov et al, 2016a, AMT)
Notes: I used the simulation of Alexander Myagkov based on the study of … and adapted this fr my study and the limit of my radar
This 2 plots represent the SLDR for zenith pointing and for 30 degrees elevation

## Slide 24
Output with Alexander Myagkov‘ Algorithm
(Myagkov et al, 2016a, AMT)
ρcx (Cross-Channel correlation), dependency with orientation and shape of ice crystals
Notes:  This 2 plots represent the cross-channel correlation for zenith pointing and for 30 degrees elevation

## Slide 25: Specific case in CyCARE (Cyprus)
RHI scan (30-90) of SLDR Mira-35 from Limassol, 1 May 2017
Notes: Time-height cross section on the left half
Rhox and SLDR stacked on right side. No need to show x-axis label and title in the upper subplot
Proposed date: 6.3.19, Punta, 06:31

## Slide 26
SLDR
ρcx
Specific case in CyCARE (Cyprus)
-13C
-13C
Mixed-phase cloud
RHI scan (30-90) of SLDR Mira-35 from Limassol, 1 May 2017
Notes: Time-height cross section on the left half
Rhox and SLDR stacked on right side. No need to show x-axis label and title in the upper subplot
Proposed date: 6.3.19, Punta, 06:31

## Slide 27
Insects detection (SLDR>-10dB)
SLDR
ρcx
Mixed-phase cloud
Specific case in CyCARE (Cyprus)
SLDR and ρcx Gradient
RHI scan (30-90) of SLDR Mira-35 from Limassol, 1 May 2017
Notes: Time-height cross section on the left half
Rhox and SLDR stacked on right side. No need to show x-axis label and title in the upper subplot
Proposed date: 6.3.19, Punta, 06:31

## Slide 28: Shape estimation
Cyprus, the 1st May 2017, 23:29 UTC
Gradient per layer of SLDR and ρcx

## Slide 29: Shape estimation
Shape and orientation estimation

## Slide 30: Work plan for the next steps
Observation part :
Phase calibration of SLDR and ρcx
Work directly with raw spectra (Metek pdm files) instead of moment data
Apply peak detection algorithms (PeakTree) to spectra of SLDR
Modelling part :
Derive radar observables from forwards models (CR-SIM)

## Slide 31: What we did so far…
Teresa Vogl | Audrey Teisseire
Participation in Jülich summer school | Participation in Cloudnet training school
Visit at OPTIMICE group in Cologne | LGS-CAR Discussion Workshop
 | Workshop Management PhD
Stay at site in Punta Arenas (1 month each) Oral and poster presentations at ISTP conference in Toulouse CR-SIM Workshop, Leipzig | 
Teresa Vogl | Audrey Teisseire
Visit Max Maahn at CIRES in Boulder | Visit Alexis Bern at EPFL in Lausanne
What we will do …
Notes: Coarse domain (test domain) with 20 km horizontal resolution  we will eventually go down to 1.2 km
MIRA and PAMTRA reflectivity (of course LIMRAD failed exactly on the day for which I have IFS data)

## Slide 32: Backup slides

## Slide 33
Punta Arenas
Leipzig
Background: Lidar obs. of regional differences in ice formation efficiency
Ansmann et al., 2009, JGR; Seifert et al., 2010, JGR;
Kanitz et al., 2011, GRL; Seifert et al., 2015, GRL
 Central Europe and Southern Chile: strong contrasts in ice formation efficiency
Derive cloud-top height and phase from long-term lidar datasets
Leap forward:
Quantify the lidar-observed contrasts with extensive ground-based instrumentation

## Slide 34: Work package 2 (PhD 1): DOPPLER SPECTRA ANALYSIS
Liquid reflectivity overlay plot
Notes: overlay

## Slide 35: Work package 2 (PhD 1): DOPPLER SPECTRA ANALYSIS
Liquid node LDR
Notes: overlay

## Slide 36: Work package 2 (PhD 1): DOPPLER SPECTRA ANALYSIS
Liquid node MDV
Notes: overlay

## Slide 37: Work package 2 (PhD 1): DOPPLER SPECTRA ANALYSIS
rimed node LDR
Notes: overlay

## Slide 38: Work package 2 (PhD 1): DOPPLER SPECTRA ANALYSIS
rimed node velocity
Notes: overlay

## Slide 39: Work package 3: Modeling
Measured 35 GHz reflectivity
Modeled 35 GHz reflectivity
spin up
Notes: Coarse domain (test domain) with 20 km horizontal resolution  we will eventually go down to 1.2 km
MIRA and PAMTRA reflectivity (of course LIMRAD failed exactly on the day for which I have IFS data)

## Slide 40: Work package 2 (PhD 1): DOPPLER SPECTRA ANALYSIS
e.g. probably rimed and liquid potpulations
Reflectivity of „rimed“ and „liquid“ populations, Punta Arenas, 2019-02-23
Notes: „riming“ node: e.g. in this spectrum the fastest and slowest peaks are more than 1.5 m/s fall velocity apart